## Slide 1: NRL: Nominal Response Library & The NRL Tool

## Slide 2: SEED Metadata
SEED headers are comprehensive with many required fields. Creating proper SEED metadata requires many details, particularly the channel response information.
The Nominal Response Library (NRL) provides a catalog of response information for many common sensors and data recorders.

## Slide 3: The IRIS Nominal Response Library
http://www.iris.edu/NRL
Verified with the manufacturer
Integrated into PDCC using NRL Tool
Flexible design for updates and merging

## Slide 4: NRL Components
Each instrument and digitizer in the NRL is represented by a SEED RESP file.
Categorized by equipment type and manufacturer
HTML web pages for detailed information not readily available elsewhere

## Slide 5: NRL Tool
Features:
Integrated into PDCC
Selection of complete instrument (sensor and data logger) from NRL
Merging NRLs (e.g. IRIS and local)

## Slide 6: How to launch NRL Tool in PDCC

## Slide 7: NRL Tool Demo
Reminders:
A channel (Blockette 052) must be selected before launching NRL Tool
NRL Tool will replace the response information for the selected channel