## Slide 1: Converting Waveform Data to Mini-SEED

## Slide 2: Mini-SEED Fundamentals
Mini-SEED is a bare time series only format designed for exchange and archiving of seismological data.
Data samples: integer and IEEE floats
Compression for integer samples
Basic state of health fields
No analysis or user-defined variables
  * Mini-SEED is not designed as an analysis format!

## Slide 3: Finding Converters
http://www.orfeus-eu.org/Software/conversion.html
http://www.iris.edu/pub/programs/converters/
http://www.passcal.nmt.edu/content/software-resources

## Slide 4: Existing Mini-SEED Converters
From Format | Program
GSE | gse2mseed [IRIS DMC], gse2seed (INT only) [ORFEUS]
SAC | sac2mseed [IRIS DMC], sac2ms [NCEDC]
SeisAn | seisan2mseed [IRIS DMC], SeisAn supports Mini-SEED
MARS 88/lite | mars2mseed [IRIS DMC]
Reftek | ref2mseed, rt2ms [IRIS PASSCAL]
SEGY | segy2mseed [IRIS PASSCAL], segy2ms [NCEDC]
SEED | rdseed [IRIS DMC]

## Slide 5: Waveform Conversion Warnings
Loss of header information due to incomplete format mapping
Loss of data sample precision due to sample format changes
Rule of thumb: convert waveform data as few times as possible

## Slide 6: Programming Resources
libmseed – A Mini-SEED library in C
http://www.iris.edu/pub/programs/
qlib2 – A Quanterra Users Group library
http://www.ncedc.org/qug/software/ucb/

## Slide 7: libmseed – Mini-SEED Programming
Allows reading and writing of Mini-SEED records
Written in C
Supports all structures of SEED 2.4 with a few minor caveats (blockette 2000 and blockette 405)
Supports all valid record lengths and big or little endian
Supports ASCII, int-16, int-32, float-32, float-64, Steim-1 and Steim-2 encoding formats for reading and writing (older encodings read-only)
Manages arbitrarily long continuous trace segments and groups of continuous trace segments composed, for example, of many Mini-SEED records
Tested on Solaris, Linux, Mac OSX and MS-Windows
Available from: http://www.iris.edu/pub/programs/

## Slide 8: Mini-SEED Handling Tools
msi - Mini-SEED Inspector
Parse and print useful information about Mini-SEED in one or many files. Including continuous segment construction, data sample printing, etc.
dataselect - Mini-SEED Data Selection
Subset, reorder and prune overlap for arbitrary sets of Mini-SEED
http://www.iris.edu/pub/programs/miniseed/
Many, many other Mini-SEED tools exist and are freely available.