## Slide 1: INTRODUCTION TO MUSTANG
Laura Hutchinson, Data Quality Analyst, IRIS DMC

## Slide 2: Quality Assurance
Is…
Important for high quality research
Useful for improving data – fixing stations, etc.
Subjective – bad for you might be good for me
  Ex. Is noise good or bad?

## Slide 3: Quality Assurance Using MUSTANG
What is MUSTANG
MUSTANG is an automated data quality assurance system that stores measurements of seismic data quality for the entire IRIS archive and makes them available to the community through standard web services.
Currently, 46 metrics are calculated.
The system is modular; new metrics can be added readily.
MUSTANG has the capability to automatically update metrics values when the data or metadata changes, and in the future, when metrics algorithm changes.

## Slide 4: MUSTANG: Quality Assurance System

## Slide 5: IRIS DMC: Enhanced Quality Assurance
MUSTANG
MUSTANG Measurements
gaps, overlaps, completeness, signal-to-noise, psd, pdf, etc (46 metrics)
PostgreSLQ
Database
Public
Data Quality Analyst (me)
Domestic & non-US Network Operators

## Slide 6: Accessing MUSTANG Metrics
Now that you know what they are, how do you get to them?

## Slide 7: Web Services
MUSTANG Metrics can be reached through IRIS web services:
http://service.iris.edu
http://service.iris.edu/mustang/
Each service provides access to some facet of our metrics catalog

## Slide 8: The URL Builder
To wildcard, either leave blank or use */?
Note: the URL updates automatically

## Slide 9: Hands-On: measurements service
Pull up the number of gaps (num_gaps) for a month of BHZ data for the IU network
Find the SNCL-days that had greater than 4 gaps
Order by the SNCL
Trickier: Get the percent_availability, num_gaps, and max_gap for a month of II.BORG.00.BH1 data. (hint: use the URL to make the call, not the URL builder)

## Slide 10: Web Services - PSDs
MUSTANG Metrics can be reached through IRIS web services:
http://service.iris.edu
http://service.iris.edu/mustang/
Each service provides access to some facet of our metrics catalog

## Slide 11
http://service.iris.edu/mustang/noise-psd/1/
*Limit 5000 psds
Handles wildcards

## Slide 12
http://service.iris.edu/mustang/noise-psd/1/query?net=IU&sta=ANMO&loc=00&cha=BHZ&quality=M&starttime=2017-09-01&endtime=2017-10-01&correct=true&format=plot&nodata=404
http://service.iris.edu/mustang/noise-psd/1/query?net=IU&sta=ANMO&loc=00&cha=BHZ&quality=M&starttime=2017-09-01&endtime=2017-10-01&correct=true&format=text&nodata=404

## Slide 13: Hands-On: PSDs
Pull up a plot of IU.ANMO.00.BHZ data for one day of data
Now do the same, but for an hour
Play with adding a title and the various Plot Options
Instead of a plot, get the results as XML and/or text
Note that PSDs are calculated for hour-long time periods, every half hour.

## Slide 14: Web Services – PSD modes
MUSTANG Metrics can be reached through IRIS web services:
http://service.iris.edu
http://service.iris.edu/mustang/
Each service provides access to some facet of our metrics catalog

## Slide 15
http://service.iris.edu/mustang/noise-mode-timeseries/1/
Single target only – no wildcarding

## Slide 16
http://service.iris.edu/mustang/noise-mode-timeseries/1/query?net=IU&sta=ANMO&loc=00&cha=BHZ&quality=M&starttime=2017-01-01&endtime=2017-10-01&output=power&format=plot&nodata=404

## Slide 17: Hands-On: PSD modes
Pull up a plot of IU.BILL.00.BHZ for 2017-03-01 to 2017-06-01
Compare that to the other Output options:
  Power values vs high-noise model
  Power values vs low-noise model
  Power values vs high- and low-noise models
Choose your own frequencies to plot
Note that you can base it off of your own noise model – which could be the noise model for that station or network, or any other model you would like.

## Slide 18: Web Services - PDFs
MUSTANG Metrics can be reached through IRIS web services:
http://service.iris.edu
http://service.iris.edu/mustang/
Each service provides access to some facet of our metrics catalog

## Slide 19
http://service.iris.edu/mustang/noise-pdf/1/
Handles long time ranges well
Allows wildcards

## Slide 20
http://service.iris.edu/mustang/noise-pdf/1/query?net=IU&sta=ANMO&loc=00&cha=BHZ&quality=M&starttime=2010-01-01&endtime=2017-10-01&format=plot&plot.interpolation=bicubic&nodata=404

## Slide 21: Hands-On: PDFs
Generate a plot of the PDF for IU.BILL.00.BHZ for 2017-03-01 to 2017-06-01
  Narrow down to determine when the change occurred
Pull up the text version of the PDF – what is each column?
Get the BHZ channels entire IU network for 2017
Get the entire history of IU.ANMO.00.BH1

## Slide 22: Web Services – PDF Browser
MUSTANG Metrics can be reached through IRIS web services:
http://service.iris.edu
http://service.iris.edu/mustang/
Each service provides access to some facet of our metrics catalog

## Slide 23
http://service.iris.edu/mustang/noise-pdf-browser/1/
http://service.iris.edu/mustang/noise-pdf-browser/1/gallery?
http://service.iris.edu/mustang/noise-pdf-browser/1/breakout?
http://service.iris.edu/mustang/noise-pdf-browser/1/summary?

## Slide 24
Breakout view – total at top with components below
Year or month on top
Month or day below
Gallery view – monthly or yearly views
Summary view – listing of start and end of PDF availability for each sncl

## Slide 25: Hands-On: PDF Browser
Look through the Service interface page at the various usages
/gallery: Get the BHZ channels entire IU network for 2017, by month
/breakout: From the previous page, click on IU.BILL.00.BHZ Apr 2017
  Explore looking at the previous/next month
  Find the day that the channel went bad in April 2017
/summary: from the Service interface page, click on a summary view example.
  What is each column?
  Click on a target – takes you to the breakout page for that SNCL

## Slide 26: More resources
http://ds.iris.edu/ds/nodes/dmc/tutorials/getting-started-with-mustang/
http://ds.iris.edu/ds/nodes/dmc/tutorials/seismic-data-quality-assurance-using-iris-mustang-metrics/
Playing around the with URL builder, Service Interface, and Help pages
Upcoming: Research Ready Data Sets (RRDS)
  Allows users to filter requests for data based upon quality assurance metrics